Monitoring Well Construction Details of Wells Used by USGS to Make Water-Table Maps

(compiled by Maura Metheny)

| Well | Ground Surface Elevation (feet, msl) | Depth to Top of Gravel Pack (feet) | Depth to Top of Screen (feet) | Depth to Bottom of Screen (feet) | Depth to Top of Gravel Pack (feet) | Total Depth of Borehole (feet) | Depth of Bedrock (feet) | Completion Date |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| BW2 | 44.2 | 31.8 | 34.5 | 44.5 | 47 | 47 |  | 08/19/83 |
| BW4 | 43.4 | 30 | 32 | 42 | 45 | 45 |  | 08/25/83 |
| BOW8 | 45.2 |  | 3 | 13 |  |  |  | 10/04/85 |
| BOW9 | 46.2 |  | 4 | 14 |  |  |  | 10/10/85 |
| BOW10 | 46.6 |  | 2.5 | 12.5 |  | 14 |  | 09/19/85 |
| BSW12 | 45.3 |  | 28.5 | 33.5 |  |  |  | 09/18/85 |
| BOW14 | 44.8 |  | 4 | 14 |  |  |  | 11/15/85 |
| G1S | 97.6 |  | 26.5 | 36.5 |  |  |  | 10/23/85 |
| G2S | 97.6 |  | 9 | 19 |  |  |  | 06/14/83 |
| G3S | 91 |  | 22 | 37 |  |  |  | 06/22/88 |
| G5S | 93.3 |  | 11 | 21 |  |  |  | 06/23/83 |
| G9S | 95 |  | 13 | 18 |  |  |  | 08/28/84 |
| G10S | 97 |  | 15 | 25 |  |  | 22 | 09/11/84 |
| G11S | 91.4 |  | 16 | 21 |  |  | 21 | 09/01/84 |
| G12S | 93.5 |  | 15 | 25 |  |  | 25 | 09/18/84 |
| G14S | 94.2 |  | 11.8 | 21.8 |  |  |  | 10/04/85 |
| G21S | 95.2 |  | 19 | 29 |  | 29.5 |  | 09/12/85 |
| G24S | 96.2 |  | 16 | 26 |  | 27 | 26 | 10/11/85 |
| G26S | 97.4 |  | 11 | 21 |  | 22.6 | 22.6 | 09/19/85 |
| G28S | 94 |  | 14.6 | 24.6 |  | 25.5 |  | 10/01/85 |
| GO1S | 73.2 |  | 8 | 18 |  |  | 18 | 10/04/84 |
| S5 | 52.5 |  | 4 | 65.5 |  | 65.5 | 55.5 |  |
| S6 | 62.2 |  | 4 | 94 |  | 94 | 84 | 07/07/81 |
| S63S | 70 | 9 | 12 | 22 | 22 | 22 |  |  |
| S67S | 83.2 | 22 | 24 | 34 | 34 | 34 |  |  |
| S70S | 70 |  | 15 | 30 | 30 | 30 |  |  |
| S71S | 71.4 | 9 | 11 | 16 | 16 | 16 |  | 02/01/85 |
| S72S | 51.2 |  | 14 | 54 | 54 | 54 |  |  |
| S73S | 52.6 | 9 | 10 | 35 | 35 | 35 |  | 01/04/85 |
| S74D | 48.2 | 70 | 73 | 88.5 | 88.5 | 88.5 | 67.5 | 01/15/85 |
| S76S | 53.4 | 13 | 15 | 65 | 65 | 65 |  | 01/23/85 |
| S77S | 44.7 | 23.5 | 25 | 30 | 30 | 30 |  | 02/18/85 |
| S78S | 45.4 | 4 | 5 | 25 | 25 | 25 |  | 02/02/85 |
| S79S | 48 | 4 | 5 | 25 | 25 | 25 |  |  |
| S80S | 48.7 | 42 | 45 | 55 | 55 | 55 |  | 11/20/84 |
| S81S | 54.7 | 8 | 10 | 20 | 20 | 20 |  | 02/08/85 |
| S84S | 45.9 | 11 | 13 | 18 | 18 | 18 |  | 03/05/85 |
| S85S | 46.1 | 18 | 20 | 30 | 30 | 62 |  | 02/26/85 |
| S86S | 44.7 | 18 | 20 | 30 | 30.5 | 62 |  | 03/06/85 |
| S87S | 45.4 |  | 7 | 9 |  |  |  | 10/02/85 |
| S88S | 44.2 |  | 7 | 9 |  |  |  | 10/11/85 |
| S89S | 43.8 |  | 29 | 31 |  |  |  | 10/09/85 |
| S90S | 47.3 |  | 7 | 9 |  |  |  | 10/01/85 |
| S91S | 44.7 |  | 7 | 9 |  |  |  | 10/02/85 |
| S92S | 43 |  | 9 | 14 |  |  |  | 11/01/85 |
| S93S | 43.4 |  | 10 | 14 |  |  |  | 10/29/85 |
| S94S | 45.8 |  | 12 | 14 |  |  |  | 10/22/85 |
| S95S | 43 |  | 9 | 14 |  |  |  | 11/09/85 |
| S96S | 43 |  | 10 | 14 |  |  |  | 10/29/85 |
| S97S | 48.9 |  | 9 | 14 |  |  |  | 11/11/85 |